# Specification Sheet

Town Center Plan A

Tract 2, Cabarrus Ave.

Stanfield NC 28163

Scope of Construction & General Conditions:

- Building Contract contingent upon financing (If applicable).

- All construction in accordance with NC Building Codes.

- Helms Builders Inc. will supply all Building, Utility Permits, and Builders Risk Insurance & Foundation Surveys.

- Planning, coordination & pricing for selections of all other materials & colors is to be completed jointly by owner & contractor.

- Helms Builders Inc. is responsible for providing County water tap & sewer.

- Homeowners will be notified of all change orders, upgrades & overages as soon as we are aware of them. Homeowner’s approval will be required prior to installation or ordering.

Footings:

- All Footings min. 12” deep x12” wide with 3000 lb. mix.

Foundation & Floor:

- Concrete turndown slab, 4” concrete w/ fiber.

Framing:

- All framing lumber #2 or better.

- Walls, 2”x4”x105” studs.

- Exterior sheathing ½” osb.

- Truss 24” oc.

- Roof sheeting 7/16” Radiant barrier osb. covered with 15lb. Builders felt.

Shingles:

- Architectural 30 yr. shingles.

- Ridge vents.

- Step flashing.

Exterior:

- Siding Vinyl Board & Batten & Horizonal Lap.

- Windows, Atrium (White) as per plans, with insulated glass, 3/4” grills between glass (as plans) & screens.

- Doors: Front & Rear doors as per. selections.

- Boxing, overhang 12” unless noted on plans. Covered with aluminum & vinyl.

- Gutters aluminum with baked on finish, OS. down spouts emptying drain tile.

Front Porch:

- Vinyl ceiling.

- 4” concrete floor.

- 8” Cedar columns

Rear Porch:

- 6” Cedar columns

- Vinyl ceiling.

- Screening

- 4” concrete floor.

Interior Trim Spec. For All Rooms:

- Sheetrock walls.

- Sheetrock ceiling ½” screwed in place with smooth finish, painted white.

- Casings 1”x4”

- Interior doors panel hollow core (style to be determined).

- Base 1x8 style.

- Painted woodwork.

Interior Trim Spec. For Individual Rooms:

Garage:

- 4” fiber reinforced concrete floor over moisture barrier.

- 1-18’x8’ paneled insulated aluminum overhead door with openers side entry.

Family Rm.:

- Laminate/LVP floor.

- Crown mold Cove

- 42” electric fireplace or equal & mantle.

- Stone to mantle, 8” nickel gap above, Farm Craft © mantle.

Halls:

- Crown mold Cove

- Laminate/LVP floor.

Kitchen & Dining:

- Laminate/LVP floor.

- Crown mold Cove

- Cabinet’s (to be selections), Quartz cabinet tops & tile backsplash.

- Kitchen sink 50/50 stainless & faucet (to be selections)..

- Appliance (to be selected)

- Electric range.

Laundry Room:

- Tile Flooring

- Shelf above washer & dryer

- Electric Dryer connection.

Drop Zone:

- Laminate/LVP floor.

Master Bedroom.

- Laminate/LVP floor.

- Crown mold Cove

Master Closet:

- Laminate/LVP floor.

- Wire shelving

Master Bath Rm.:

- Tile floor.

- Cabinets (to be selected) 36” with quartz top, rectangle undermount sinks, plumbing per. selection, with mirror above.

- Shower 42”x72”, faucet as per. (owner’s selections), and shower walls with clear glass. Corner seat out of Quartz.

Guest Bath:

- Tile floor

- Cabinets 36” with quartz top, oval undermount sinks, faucet as per. (owner’s selections). with mirror above.

- Tub 60” fiberglass unit.

Bed Rms.: 2, 3

- Laminate/LVP floor.

Paint & Finish:

- All interior walls will be primed and have 2 coats of flat latex wall paint.

- Walls include 3 colors

- All interior trim will be primed and have 3 coats of latex trim paint.

Plumbing:

- 1-50 gal. Electric hot water heater.

- All supplies poly

- PVC drains (except down walls).

- Two hose bibs.

- Plumbing fixture (to be selected by owners).

- All vents on back of house.

Heating Equipment

- Trane one unit, 14 seer Dual speed. Zoned, Air-condition, Heat pump.

- All Plenums will be galvanized with joints covered with mastic.

- All the Ducts from the plenums will be Foil backed flexes with mastic joints.

- 1st. Floor registers will be in ceiling.

- There will be centrally located returns on each floor. (Or as code requires)

Electrical:

- 200 amp. Service.

- Prewire 2 phones 4 strand twisted wire.

- Prewire 5 cable jacks.

- Prewire & install 5 ceiling fans.

- Prewire 4 flood lights

- 20 amp. Circuit for welder

- Smoke & Carbon Monoxide detectors, as code requires.

- Lights in attic & crawl as per code.

- All switches will be rocker style.

- Lighting allowances include light fixtures, can lights, ceiling fans, under & over counter lights, doorbell chimes and components.

Driveway:

- 4” concrete with broom finish 20’x20’ at garage (allowance item).

Sidewalk:

- 4’ wide to front door

Yard Work & Shrubs:

- Yard is to be seeded and strayed.

- Shrubs, including ground cover, plants, labor.

- Allowance item.

Other Features:

- Insulation: Walls R-15, Ceilings R-30, and Floors R-19.

- Door hardware Schlage lever (satin nickel finish) with dead bolts.

- Exterior will be pressure cleaned before closing.

- All shelves are to be metal with vinyl coated.

House Size:

- Total Heated Area					       1715     sq. ft.

- Rear Porch						        127      sq. ft.

- Front Porch						        118	      sq. ft

- Garage 		 					        576      sq. ft

- Total Under Roof					       2536     sq. ft.

Change Orders:

- Must be signed by both parties.

- Must be paid for prior to installation.

Warranty Schedule:

- There will be two-scheduled walk through, the 1st. should occur at app. 90 days after occupying home, the 2nd. should occur at the end of the first year. Homeowners should contact the superintendent that oversaw their job to schedule this.

Allowances:

- Light fixtures including recess			$4000.00

- Laminate/LVP Flooring:				$10,400.00

- Tile Materials & Labor: 				$7300.00

- Plumbing fixtures:				$2700.00

- Cabinets						$10,436.00

- Kitchen & Bath Tops:				$6000.00

- Appliances:					$3065.00

- Shelving:					$2200.00

- Concrete driveway & sidewalks:			$4700.00

- Garage Doors:					$3600.00

- Landscaping:					$6250.00

- Items included with landscape.

- Landscape plans for arc. approval

- Gutter drains

- Seeding yard

- Prep. Natural areas

- Plant beds, plants, shrubs & ground cover.

Price Submitted:  $359,500.00 ($65,000 Lot cost included in price)

Price void after 30 days.

I agree that I have read the above document and understand it fully, and this will become a pertinent

part of the final contract upon signing below.